## Slide 1: CSC 144V: Autonomous Vehicles Lecture 5 Object Detection and Segmentation Exercises Solution
Department of Computer Science,
Hofstra University

## Slide 2: Exercise: IoU and NMS
Four detections of two pedestrians, boxes (x₁, y₁, x₂, y₂) in pixels. IoU = |A ∩ B| / |A ∪ B|.
(a) Compute the IoU of each box with the top-scoring box A. (b) Run greedy NMS: keep the best box, suppress boxes with IoU > threshold with a kept box. Threshold 0.5. (c) Which boxes remain with threshold 0.4?
Box | (x₁, y₁, x₂, y₂) | Score | IoU with A | NMS, thr. 0.5
A | (10, 10, 60, 60) | 0.9 |  | 
B | (20, 20, 70, 70) | 0.8 |  | 
C | (12, 12, 62, 62) | 0.7 |  | 
D | (100, 100, 150, 160) | 0.6 |  | 

## Slide 3: Exercise Solution: IoU and NMS
IoU(A, B): intersection 40 × 40 = 1,600, union 2,500 + 2,500 − 1,600 = 3,400 → 0.47. IoU(A, C): 48 × 48 = 2,304, union 2,696 → 0.85. IoU(A, D) = 0.
Threshold 0.5: keep A; suppress C (0.85); B survives (0.47 ≤ 0.5); D survives → A, B, D.
Threshold 0.4: B is also suppressed (0.47 > 0.4) → A, D. A low threshold risks removing a second object that overlaps the first.
Box | (x₁, y₁, x₂, y₂) | Score | IoU with A | NMS, thr. 0.5 | NMS, thr. 0.4
A | (10, 10, 60, 60) | 0.9 | 1 | keep | keep
B | (20, 20, 70, 70) | 0.8 | 0.47 | keep | suppress
C | (12, 12, 62, 62) | 0.7 | 0.85 | suppress | suppress
D | (100, 100, 150, 160) | 0.6 | 0 | keep | keep

## Slide 4: Calculating IoU(A, B)
The coordinates of the boxes are (lower left corner and upper right corner):
  Box A: (10,10,60,60)
  Box B: (20,20,70,70)
Each box has a width and height of 50, so each has an area of:
  Area(A)=50×50=2500
  Area(B)=50×50=2500
Step 1: Calculate the intersection.
  The overlapping region extends from coordinate 20 to 60 on both axes, with width and height both 40
  Intersection=40×40=1600
Step 2: Calculate the union.
  Subtract the overlapping area from the sum of both box areas:
  Union=2500+2500−1600=3400​
Step 3: Calculate IoU.
  IoU(A,B)=1600/3400≈0.47​
This means the boxes have approximately 47% overlap relative to their combined area.

## Slide 5: Exercise: Precision, recall and AP
There are 5 ground-truth objects. The detector returns 6 detections sorted by confidence: TP, TP, FP, TP, FP, TP.
(a) Precision and recall after each rank.
(b) Average precision using the all-point interpolated envelope: precision at recall r is the maximum precision at any recall ≥ r.
Rank | TP / FP | Precision | Recall
1 | TP |  | 
2 | TP |  | 
3 | FP |  | 
4 | TP |  | 
5 | FP |  | 
6 | TP |  | 

## Slide 6: Exercise Solution: Precision, recall and AP
Precision = TP/rank; recall = TP/5.
Envelope: recall 0.2 → 1, 0.4 → 1, 0.6 → 0.75, 0.8 → 0.667, 1.0 → 0 (never reached).
AP = 0.2 × (1 + 1 + 0.75 + 0.667 + 0) ≈ 0.683.
Rank | TP / FP | Precision | Recall
1 | TP | 1.00 | 0.2
2 | TP | 1.00 | 0.4
3 | FP | 0.67 | 0.4
4 | TP | 0.75 | 0.6
5 | FP | 0.60 | 0.6
6 | TP | 0.67 | 0.8

## Slide 7: Exercise: YOLO label of a grid cell
A 300 × 300 image is divided into a 3 × 3 grid; classes: Pedestrian, Car, Motorcycle. A car has its mid-point at pixel (170, 240); its box is 150 px wide and 60 px high.
(a) Which grid cell (row, col from 0, top-left) is responsible?
(b) Fill in the label y = (pc, bx, by, bh, bw, c₁, c₂, c₃) of that cell.
(c) What is the shape of the whole output tensor?
pc | bx | by | bh | bw | c₁ | c₂ | c₃

## Slide 8: Exercise Solution: YOLO label of a grid cell
(a) Cell size 100 px: col = ⌊170/100⌋ = 1, row = ⌊240/100⌋ = 2 → cell (2, 1).
(b) bx = (170 − 100)/100 = 0.7, by = (240 − 200)/100 = 0.4, bh = 60/100 = 0.6, bw = 150/100 = 1.5 (can exceed 1). Car is class 2.
(c) 8 numbers per cell: 3 × 3 × 8.
pc | bx | by | bh | bw | c₁ | c₂ | c₃
1 | 0.7 | 0.4 | 0.6 | 1.5 | 0 | 1 | 0

## Slide 9: Exercise: Realistic YOLO dimensions
A realistic YOLO takes a 608 × 608 × 3 image and outputs a 19 × 19 × 5 × 85 tensor.
(a) What do 5 and 85 stand for?
(b) How many numbers are predicted, and how many candidate boxes enter NMS?
(c) What is the stride (pixels per grid cell)? In which cell (row, col from 0) does an object with mid-point at pixel (330, 200) fall, and what are (bx, by) of its label?

## Slide 10: Exercise Solution: Realistic YOLO dimensions
(a) 5 anchor boxes per cell; 85 = 5 + 80: (pc, bx, by, bh, bw) plus 80 class scores.
(b) 19 × 19 × 5 × 85 = 153,425 numbers; 19 × 19 × 5 = 1,805 candidate boxes before NMS.
(c) Stride 608/19 = 32 px. col = ⌊330/32⌋ = 10, row = ⌊200/32⌋ = 6 → cell (6, 10); bx = (330 − 320)/32 = 0.31, by = (200 − 192)/32 = 0.25.

## Slide 11: Exercise: Upsampling
Upsample the 2 × 2 feature map to 4 × 4 with a stride of 2.
(a) Bed of nails: insert zeros; each input goes to the top-left corner of its 2 × 2 block.
(b) Nearest neighbor: duplicate each element.
(c) Name two other upsampling methods used in FCNs.
Input (2 × 2)
1 | 2
3 | 4
Bed of nails (4 × 4)
Nearest neighbor (4 × 4)

## Slide 12: Exercise Solution: Upsampling
(a) Bed of nails keeps the values at fixed positions and fills the rest with 0.
(b) Nearest neighbor replicates each value over its 2 × 2 block.
(c) Max unpooling (restores each value to the position of the max in the matching pooling layer), bilinear / bicubic interpolation, transposed convolution (learnable).
Input (2 × 2)
1 | 2
3 | 4
Bed of nails (4 × 4)
Nearest neighbor (4 × 4)
1 | 0 | 2 | 0
0 | 0 | 0 | 0
3 | 0 | 4 | 0
0 | 0 | 0 | 0
1 | 1 | 2 | 2
1 | 1 | 2 | 2
3 | 3 | 4 | 4
3 | 3 | 4 | 4

## Slide 13: Exercise: Transposed convolution
Transposed convolution (stride 1, no padding): each input element multiplies the whole kernel, the products are placed at its position, and overlapping outputs add up.
(a) Compute the 3 × 3 output.
(b) Output size formula for input N, kernel K, stride S?
(c) With L stacked 3 × 3 CONV layers (stride 1) the receptive field is 2L + 1. For L = 10? How many layers for a receptive field ≥ 224? How does downsampling help?
Input
1 | 2
3 | 4
Kernel
1 | 2
0 | 1
Output (3 × 3)

## Slide 14: Exercise Solution: Transposed convolution
(a) e.g. O[1][1] = 1·1 + 2·0 + 3·2 + 4·1 = 11 (four overlapping contributions).
(b) (N − 1)·S + K = (2 − 1)·1 + 2 = 3.
(c) L = 10 → 21 × 21. 2L + 1 ≥ 224 → L ≥ 111.5 → 112 layers: too slow. Pooling / strided convolution makes the receptive field grow much faster and shrinks the cost; upsampling then restores the output size.
Input
1 | 2
3 | 4
Kernel
1 | 2
0 | 1
Output (3 × 3)
1 | 4 | 4
3 | 11 | 10
0 | 3 | 4