## Slide 1: CSC 144V: Autonomous Vehicles Lecture 10 AD with IL and RL Exercises Solution
Department of Computer Science,
Hofstra University

## Slide 2: Exercise: Compounding error in BC
Behavior cloning (BC) suffers from distribution shift: the learner makes a small error with probability ε per step and then visits states the expert never showed. Cost 1 per mistake, horizon T = 100, ε = 0.002.
(a) Expected total cost if errors did not compound (i.i.d. supervised bound ε T)?
(b) BC bound ε T²? Ratio?
(c) Why do errors compound? Name two remedies used in practice.
Setting | Expected cost
Errors independent (ε T) | 
BC with compounding (ε T²) | 
Ratio | 

## Slide 3: Exercise Solution: Compounding error in BC
(a) ε T = 0.002 · 100 = 0.2.
(b) ε T² = 0.002 · 10,000 = 20: T = 100 times larger.
(c) One mistake puts the car in a state (off-center) that is not in the expert data, so the next action is also unreliable, and errors accumulate quadratically with the horizon.
Remedies: data augmentation with shifted and rotated views and corrective labels (PilotNet); DAgger (query the expert on the learner’s own states); also adding noise to the expert’s demonstrations.
Setting | Expected cost
Errors independent (ε T) | 0.2
BC with compounding (ε T²) | 20
Ratio | 100×

## Slide 4: Exercise: Augmentation labels
PilotNet predicts the inverse turning radius 1/r. A synthetic image shows the car e = 0.5 m left of the lane center; the label should bring the car back to the center within 2 s at v = 10 m/s. Left turns are positive.
(a) Distance driven in 2 s? Approximating the correction by a circular arc, e = κ d²/2: what curvature κ = 1/r is needed, and what radius?
(b) Steering label of the shifted image if the human drove straight (label 0)?
(c) The needed wheel angle for L = 2.8 m (δ = atan(Lκ))? And κ for e = 1.0 m?

## Slide 5: Exercise Solution: Augmentation labels
(a) d = 10 × 2 = 20 m; κ = 2e/d² = 2 · 0.5/400 = 0.0025 m⁻¹, i.e. r = 400 m.
(b) The car is left of center, so it must turn right: label = −0.0025 m⁻¹ (added to the human’s own 1/r).
(c) δ = atan(2.8 · 0.0025) = atan(0.007) ≈ 0.007 rad ≈ 0.4°; for e = 1.0 m: κ = 0.005 m⁻¹.
Left and right cameras (and synthetic shifts and rotations) give recovery examples the human never produced.

## Slide 6: Exercise: PilotNet architecture
PilotNet: input 66 × 200 × 3 (YUV), a normalization layer (no learnable parameters), 5 convolutional layers, 3 FC layers and one output. Fill in the output shape and the number of parameters of each layer.
Layer | Configuration | Output shape | # parameters
Conv1 | 5×5, stride 2, 24 filters |  | 
Conv2 | 5×5, stride 2, 36 filters |  | 
Conv3 | 5×5, stride 2, 48 filters |  | 
Conv4 | 3×3, stride 1, 64 filters |  | 
Conv5 | 3×3, stride 1, 64 filters |  | 
FC1 | 1152 → 100 |  | 
FC2 | 100 → 50 |  | 
FC3 | 50 → 10 |  | 
Output | 10 → 1 |  | 

## Slide 7: Exercise Solution: PilotNet architecture
Output size = ⌊(N − F)/S⌋ + 1. Total = 252,219 parameters (≈ 250 k): 131,348 in the convolutions and 120,871 in the FC layers.
Layer | Configuration | Output shape | # parameters
Conv1 | 5×5, stride 2, 24 filters | 31 × 98 × 24 | 1,824
Conv2 | 5×5, stride 2, 36 filters | 14 × 47 × 36 | 21,636
Conv3 | 5×5, stride 2, 48 filters | 5 × 22 × 48 | 43,248
Conv4 | 3×3, stride 1, 64 filters | 3 × 20 × 64 | 27,712
Conv5 | 3×3, stride 1, 64 filters | 1 × 18 × 64 | 36,928
FC1 | 1152 → 100 | 100 | 115,300
FC2 | 100 → 50 | 50 | 5,050
FC3 | 50 → 10 | 10 | 510
Output | 10 → 1 | 1 | 11

## Slide 8: Exercise: Reward ambiguity in IRL
Inverse RL: chain S1, S2, S3. The expert goes S1 → S2 → S3. The alternative stays at S1 twice. Return of a path = R(first state entered) + 0.9 · R(second state entered).
(a) For each candidate reward (R(S1), R(S2), R(S3)) compute both returns: is the expert behavior optimal?
(b) What does this show about the reward function recovered by IRL?
Reward (S1, S2, S3) | Expert return | Alternative return | Expert optimal?
a: (0, 0, 1) |  |  | 
b: (0, 0, 5) |  |  | 
c: (0, 0.5, 1) |  |  | 
d: (0, 0, 0) |  |  | 
e: (1, 0, 0) |  |  | 
f: (1, 1, 2) |  |  | 

## Slide 9: Exercise Solution: Reward ambiguity in IRL
Rows a, b, c, d, f are all consistent with the expert; only e is not (it rewards staying at S1).
(b) The reward is not unique: scaling (b = 5 × a), shifting (f) and even R ≡ 0 (d: every behavior is optimal) explain the demonstrations. IRL needs extra assumptions (e.g. max-margin or max-entropy) to pick one.
Reward (S1, S2, S3) | Expert return | Alternative return | Expert optimal?
a: (0, 0, 1) | 0.9 | 0 | yes
b: (0, 0, 5) | 4.5 | 0 | yes
c: (0, 0.5, 1) | 1.4 | 0 | yes
d: (0, 0, 0) | 0 | 0 | yes (tie)
e: (1, 0, 0) | 0 | 1.9 | no
f: (1, 1, 2) | 2.8 | 1.9 | yes